## Slide 1
PROJECT REVIEW
Predictive Digital Twin
A Full-Stack Simulation Framework for
ML-Optimized Industrial Gateways (Modbus/GSM/4G)
Industrial IoT • Digital Twin • Machine Learning • Network Simulation

## Slide 2
PROJECT OVERVIEW
What is this project?
This project develops a software-defined Predictive Digital Twin framework for industrial communication gateways. The system simulates end-to-end Modbus RTU/TCP communication over Ethernet and cellular networks (GSM/4G) in a fully virtualized environment.
The framework models real-world network impairments such as latency, jitter, and packet loss, and uses machine learning to predict optimal gateway parameters like polling rate and buffer size to improve communication reliability.
The entire system is implemented as a software simulation environment without requiring physical PLC hardware.
Protocol Emulation
Virtualized PLC nodes & gateway logic
Network Modeling
Real-world 4G/GSM link impairments
ML Optimization
Predictive models for gateway tuning
Analytics Dashboard
Real-time performance visualization

## Slide 3
Motivation (5 Marks)
Industrial Communication Gap
Legacy Modbus RTU/TCP systems lack native support for modern cellular networks (GSM/4G), creating integration and reliability challenges in industrial IoT deployments.
Hardware Testing Cost
Gateway testing using physical PLCs, routers, and network equipment is expensive and time-consuming. A virtualized simulation framework reduces cost and development time.
Need for Adaptive Gateway Configuration
Static polling configurations fail under variable network conditions such as latency and packet loss. Machine learning models can dynamically tune gateway parameters for reliable communication.
Need for Network Performance Visibility
Industrial operators require real-time monitoring of communication metrics such as latency, jitter, throughput, and packet loss to ensure system reliability and uptime.

## Slide 4
Objectives
01
Emulate Modbus RTU/TCP protocol stack using virtualized PLC nodes and central gateway logic
02
Simulate realistic 4G/GSM network impairments (latency, jitter, packet loss) using Linux Traffic Control (tc)
03
Develop ML models (Scikit-learn / TensorFlow) to forecast network quality and tune gateway parameters adaptively
04
Build a FastAPI backend to stream real-time telemetry and expose RESTful APIs for simulation metrics
05
Create a React.js (Vite) dashboard with WebSocket/MQTT for live performance monitoring and ML accuracy evaluation

## Slide 5
Problem Survey
Protocol
Fragmentation
Modbus RTU is serial-only; bridging to TCP/IP and cellular requires complex multi-layer translation not supported natively.
Network
Impairment
Realism
Existing simulators fail to replicate real-world 4G/GSM link behavior including dynamic jitter and burst packet loss patterns.
Static Gateway
Configuration
Industrial gateways use fixed polling intervals which perform poorly under variable network quality, increasing latency and failure rates.
Observability
Deficit
No standardized, open-source dashboard exists for monitoring Modbus-over-cellular communication quality in real time.

## Slide 6
Knowledge Gained on the Topic
1. Modbus & Industrial Communication
2. Network Impairments & Cellular Communication
Digital Twin Simulation
Machine Learning Optimization
Modbus RTU vs Modbus TCP communication
Master–Slave polling mechanism
Frame structure and register addressing
Protocol conversion (Serial → TCP → Cellular)
Latency, jitter, packet loss modeling
GSM/4G network behavior and link variability
Impact of network conditions on polling-based protocols
Virtual device and gateway emulation
Simulation of real-world network conditions
Performance analysis using simulation environments
Time-series telemetry data processing
Network quality prediction using ML models
Adaptive tuning of gateway polling parameters

## Slide 7
Progress in Work
Completed
Virtual PLC & Gateway Setup
Docker Compose stack with isolated Modbus RTU/TCP nodes deployed and operational.
100%
Completed
Network Impairment Emulation
Linux tc rules for latency (50-200ms), jitter (±30ms), and packet loss (1-5%) configured.
100%
In Progress
ML Prediction Model
Training dataset collected from emulation. Scikit-learn regression model under training.
65%
In Progress
FastAPI Backend
REST endpoints for telemetry exposed. WebSocket streaming under integration testing.
70%
Planned
React Dashboard
UI wireframes finalized. Component development begins after backend API stabilization.
20%

## Slide 8
Technology Stack
OS & Virtualization
Ubuntu 22.04 LTS
Docker
Docker Compose
Protocol Emulation
Modbus RTU/TCP
Pymodbus Library
Virtual PLC Nodes
Network Simulation
Linux tc
4G/GSM Impairments
Jitter & Packet Loss
Machine Learning
Scikit-learn
TensorFlow
pandas / NumPy
Backend
FastAPI
REST APIs
WebSockets / MQTT
Frontend
React.js (Vite)
Real-time Dashboard
Performance Charts

## Slide 9
SUMMARY
This project proposes a Predictive Digital Twin framework for industrial Modbus gateways operating over GSM/4G networks.
The system simulates Modbus communication, protocol conversion, and cellular network impairments in a fully virtual environment.
Machine Learning models are used to predict network quality and optimize gateway parameters such as polling rate and buffer size.
The system includes a real-time analytics dashboard for monitoring communication performance.
The framework helps reduce hardware testing cost, improve reliability, and optimize industrial IoT gateway performance.
Future work includes ML model improvement, full system integration, and performance evaluation under different network conditions.